Fiat 500L Technical Specifications

|  | 0.9 TwinAir 105hp | 1.4 95hp | 1.3 MultiJet 85hp | 1.3 MultiJet 85hp MTA | 1.6 MultiJet 105hp |
| --- | --- | --- | --- | --- | --- |
| Brakes |  |  |  |  |  |
| Front Brakes: | Ventilated Disc | Ventilated Disc | Ventilated Disc | Ventilated Disc | Ventilated Disc |
| Rear Brakes: | Disc | Disc | Disc | Disc | Disc |
| Dimensions |  |  |  |  |  |
| Front Track (mm): | 1522 | 1522 | 1522 | 1522 | 1522 |
| Height (mm): | 1667 | 1667 | 1667 | 1667 | 1667 |
| Length (mm): | 4147 | 4147 | 4147 | 4147 | 4147 |
| Rear Track (mm): | 1519 | 1519 | 1519 | 1519 | 1519 |
| Wheelbase (mm): | 2612 | 2612 | 2612 | 2612 | 2612 |
| Width (mm): | 1784 | 1784 | 1784 | 1784 | 1784 |
| Electrical system |  |  |  |  |  |
| Battery capacity (Ah): | 63 | 50 | 63 | 63 | 72 |
| Engine characteristics |  |  |  |  |  |
| Camshaft Drive: | Toothed Belt | Toothed Belt | Chain | Chain | Toothed Belt |
| Camshaft: | SOHC | DOHC | DOHC | DOHC | DOHC |
| Compression ratio: | 10.0 : 1 | 11.0 : 1 | 16.8 : 1 | 16.8 : 1 | 16.5 : 1 |
| Engine Capacity (cc): | 875 | 1368 | 1248 | 1248 | 1598 |
| Fuel Type: | Petrol | Petrol | Diesel | Diesel | Diesel |

Fiat 500L Technical Specifications contd.

|  | 0.9 TwinAir 105hp | 1.4 95hp | 1.3 MultiJet 85hp | 1.3 MultiJet 85hp MTA | 1.6 MultiJet 105hp |
| --- | --- | --- | --- | --- | --- |
| Engine characteristics contd. |  |  |  |  |  |
| Ignition: | Electronic multipoint injection, turbo charger with intercooler | Electronic multipoint injection | By Compression Common Rail, direct injection with MultiJet II system, turbocharger with intercooler | By Compression Common Rail, direct injection with MultiJet II system, turbocharger with intercooler | By Compression Common Rail, direct injection with MultiJet II system, turbocharger with intercooler |
| Drive | 8 valves | 16 valves | 16 valves | 16 valves | 16 valves |
| No. of Cylinders: | 2 in line | 4 in line | 4 in line | 4 in line | 4 in line |
| Number of Valves per Cylinder: | 4 | 4 | 4 | 4 | 4 |
| Start&Stop System | YES | NO | YES | YES | YES |
| Max Power (bhp): | 105 | 95 | 85 | 85 | 105 |
| Max Power (KW): | 77 | 70 | 62 | 62 | 77 |
| Power (@ rpm): | 5500 | 6000 | 3500 | 3500 | 3750 |
| Torque (@rpm): | 2000 | 4500 | 1500 | 1500 | 1750 |
| Torque (Kgm): | 14.8 | 12.9 | 20.4 | 20.4 | 32.6 |
| Torque (Nm): | 145 | 127 | 200 | 200 | 320 |
| Performance |  |  |  |  |  |
| Acceleration 0-62 mph (sec): | 12.3 | 12.8 | 14.9 | 15.1 | 11.3 |
| CO2 emissions: | 112 | 145 | 110 | 105 | 117 |
| Emission levels: | Euro 6 | Euro 6 | Euro 5+ | Euro 5+ | Euro 5+ |
| Fuel Consumption Combined (mpg): | 4.8 (58.9) | 6.2 (45.6) | 4.2 (67.3) | 4.0 (70.6) | 4.5 (62.8) |

Fiat 500L Technical Specifications contd.

|  | 0.9 TwinAir 105hp | 1.4 95hp | 1.3 MultiJet 85hp | 1.3 MultiJet 85hp MTA | 1.6 MultiJet 105hp |
| --- | --- | --- | --- | --- | --- |
| Performance contd. |  |  |  |  |  |
| Fuel Consumption Extra Urban (mpg): | 4.3 (65.7) | 5.0 (56.5) | 3.7 (76.3) | 3.7 (76.3) | 3.9 (72.4) |
| Fuel Consumption Urban (mpg): | 5.7 (49.6) | 8.3 (34.0) | 5.0 (56.5) | 4.5 (62.8) | 5.4 (52.3) |
| Top Speed (mph): | 112 | 111 | 102 | 102 | 112 |
| Top Speed (km/h): | 180 | 178 | 164 | 164 | 181 |
| Steering |  |  |  |  |  |
| Steering: | Rack-and-pinion with Electric Power Assistance Dualdrive™ with city mode | Rack-and-pinion with Electric Power Assistance Dualdrive™ with city mode | Rack-and-pinion with Electric Power Assistance Dualdrive™ with city mode | Rack-and-pinion with Electric Power Assistance Dualdrive™ with city mode | Rack-and-pinion with Electric Power Assistance Dualdrive™ with city mode |
| Turning Circle (m): (wall-to-wall) | 11.1 | 11.1 | 11.1 | 11.1 | 11.1 |
| Suspension system |  |  |  |  |  |
| Front suspension: | Independent, MacPherson strut type | Independent, MacPherson strut type | Independent, MacPherson strut type | Independent, MacPherson strut type | Independent, MacPherson strut type |
| Rear Suspension: | Semi-independent, Torsion Beam | Semi-independent, Torsion Beam | Semi-independent, Torsion Beam | Semi-independent, Torsion Beam | Semi-independent, Torsion Beam |

Fiat 500L Technical Specifications contd.

|  | 0.9 TwinAir 105hp | 1.4 95hp | 1.3 MultiJet 85hp | 1.3 MultiJet 85hp MTA | 1.6 MultiJet 105hp |
| --- | --- | --- | --- | --- | --- |
| Transmission |  |  |  |  |  |
| Drive Type: | Front | Front | Front | Front | Front |
| Gearbox: | Manual | Manual | Manual | Dualogic | Manual |
| Number of Gears: | 6 speed | 6 speed | 5 speed | 5 speed semi-automatic | 6 speed |
| Tyres |  |  |  |  |  |
| Front Tyres: | 205/55 R16 | 205/55 R16 | 205/55 R16 | 205/55 R16 | 205/55 R16 |
| Rear Tyres: | 205/55 R16 | 205/55 R16 | 205/55 R16 | 205/55 R16 | 205/55 R16 |
| Weights and capacities |  |  |  |  |  |
| Fuel tank capacity (l): | 50 | 50 | 50 | 50 | 50 |
| Kerb weight: | 1260 | 1245 | 1315 | 1320 | 1365 |
| Towable weight (non braked) | 400 | 400 | 400 | 400 | 400 |
| Towable weight (braked) | 1000 | 1000 | 1000 | 1000 | 1100 |

Fiat 500L Standard Equipment

|  |  | Popstar | Easy | Lounge |
| --- | --- | --- | --- | --- |
| All 500Ls will offer as standard: 5” Touchscreen radio, body coloured electric door mirrors, Bluetooth, cruise control, A/C, 6 airbags, spare wheel, ESP |  | 5” Touchscreen radio |
|  |  | Bluetooth |
|  |  | 6 Airbags |
|  |  | ESP |
|  |  | Body coloured electrically adjustable door mirrors |
|  |  | Cruise control |
|  |  | Leather shift knob/ Steering wheel |
| Pop Star and Easy = same price |  | Cargo box |
|  |  | Spare wheel |
|  |  | A/C | Auto A/C |
|  |  | 16” Alloy | 16” Steel | 16” Alloy |
| Lounge: + £1,400 with £2,000 customer value |  | Mouldings |  | Mouldings |
|  |  |  | Rear parking sensors |
|  |  |  | Electric rear windows |
|  |  |  |  | Glass roof |
|  |  |  |  | Light sensor |
| 0.9 TwinAir (petrol) and 1.3 MultiJet (diesel) = same price (+£1,500 vs 1.4 Petrol) |  |  |  | Rain sensor |
|  |  |  |  | Foglights |
|  |  |  |  | Rear armrest |

Fiat 500L: Model Specification

| Model | No. Doors | CO2 g/km | Basic Price £ | VAT £ | Total Retail £ | OTR Charges £ | Total OTR £ |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1.4 Pop Star (95hp) | 5-door | 145 | 11,959.12 | 2391.82 | 14,350.94 | 639.06 | 14,990.00 |
| 0.9 TwinAir PopStar (105hp) | 5-door | 112 | 13,321.62 | 2664.32 | 15,985.94 | 504.06 | 16,490.00 |
| 1.3 MultiJet Pop Star (85hp) | 5-door | 110 | 13,321.62 | 2664.32 | 15,985.94 | 504.06 | 16,490.00 |
| 1.3 MultiJet MTA Pop Star (85hp) | 5-door | TBC | 14,071.62 | 2814.32 | 16,885.94 | 504.06 | 17,390.00 |
| 1.6 MultiJet Pop Star (105hp) | 5-door | TBC | 14,154.95 | 2830.99 | 16,985.94 | 504.06 | 17,490.00 |
| 1.4 Easy (95hp) | 5-door | 145 | 11,959.12 | 2391.82 | 14,350.94 | 639.06 | 14,990.00 |
| 0.9 TwinAir Easy (105hp) | 5-door | 112 | 13,321.62 | 2664.32 | 15,985.94 | 504.06 | 16,490.00 |
| 1.3 MultiJet Easy (85hp) | 5-door | 110 | 13,321.62 | 2664.32 | 15,985.94 | 504.06 | 16,490.00 |
| 1.3 MultiJet MTA Easy (85hp) | 5-door | TBC | 14,071.62 | 2814.32 | 16,885.94 | 504.06 | 17,390.00 |
| 1.6 MultiJet Easy (105 hp) | 5-door | TBC | 14,154.95 | 2830.99 | 16,985.94 | 504.06 | 17,490.00 |
| 1.4 Lounge (95hp) | 5-door | 145 | 13,125.78 | 2625.16 | 15,750.94 | 639.06 | 16,390.00 |
| 0.9 TwinAir Lounge (105hp) | 5-door | 112 | 14,488.28 | 2897.66 | 17,385.94 | 504.06 | 17,890.00 |
| 1.3 MultiJet Lounge (85hp) | 5-door | 110 | 14,488.28 | 2897.66 | 17,385.94 | 504.06 | 17,890.00 |
| 1.3 MultiJet MTA Lounge (85hp) | 5-door | TBC | 15,238.28 | 3047.66 | 18,285.94 | 504.06 | 18,790.00 |
| 1.6 MultiJet Lounge (105hp) | 5-door | TBC | 15,321.62 | 3064.32 | 18,385.94 | 504.06 | 18,890.00 |

Fiat 500L: Prices

Fiat 500L: Option Pricing

|  | Pop Star | Easy | Lounge |
| --- | --- | --- | --- |
| OPTION | Basic Price | RRP | Basic Price | RRP | Basic Price | RRP |
| Rear electric windows | £166.67 | £200 | ( | ( | ( | ( |
| Dark tinted windows | £125.00 | £150 | £125.00 | £150 | £125.00 | £150 |
| Fog lights | £133.33 | £160 | £133.33 | £160 | ( | ( |
| Automatic dual zone climate control | £203.30 | £250 | £208.30 | £250 | ( | ( |
| Heated front windscreen | £291.67 | £350 | £291.67 | £350 | £291.67 | £350 |
| Rear armrest | £125.00 | £150 | £125.00 | £150 | ( | ( |
| Automatic light with rain sensors | £125.00 | £150 | £125.00 | £150 | ( | ( |
| Floor mats | £41.67 | £50 | £41.67 | £50 | ( | ( |
| Electric sunroof | £791.67 | £950 | £791.67 | £950 | £375.00 | £450 |
| Electrochromatic dipping rear view mirror | £83.33 | £100 | £83.33 | £100 | ( | ( |
| Heated front seats | £125.00 | £150 | £125.00 | £150 | £125.00 | £150 |
| Height adjustable passenger seat | £83.33 | £100 | £83.33 | £100 | £83.33 | £100 |
| Passenger seat lumbar adjustment | £83.33 | £100 | £83.33 | £100 | £83.33. | £100 |
| HiFi by Beats | £500.00 | £600 | £500.00 | £600 | £500.00 | £600 |
| Rear parking sensors | £225.00 | £270 | ( | ( | ( | ( |
| 3 rear head restraints | £41.67 | £50 | £41.67 | £50 | ( | ( |
| Fixed glass roof | £416.67 | £500 | £416.67 | £500 | ( | ( |
| Locking wheel nuts (link with alloy wheels) | ( | ( | £0.00 | £0 | ( | ( |
| Front seats with foldable table and seat pocket on back | £83.33 | £100 | £83.33 | £100 | ( | ( |
| Specific side mouldings with chrome inserts | ( | ( | £83.33 | £100 | ( | ( |
| Driver’s seat lumbar adjustment | £83.33 | £100 | £83.33 | £100 | £83.33 | £100 |
| Rear view child view mirror | £41.67 | £50 | £41.67 | £50 | - | - |
| Driver’s seat with armrest | £83.33 | £100 | £83.33 | £100 | £83.33 | £100 |
| 5” touchscreen radio with Bluetooth & DAB | £83.33 | £100 | £83.33 | £100 | £83.33 | £100 |
| Smoking kit | £41.67 | £50 | £41.67 | £50 | £41.67 | £50 |

Fiat 500L: Option Pricing

|  | Pop Star | Easy | Lounge |
| --- | --- | --- | --- |
| OPTION | Basic Price | RRP | Basic Price | RRP | Basic Price | RRP |
| Wheels |  |  |  |  |  |  |
| 17” Dark Grey alloy wheels | £250.00 | £300 | £500.00 | £600 | £250.00 | £300 |
| 16” Silver alloy wheels | - | - | £250.00 | £300 | ( | ( |
| 16” Alloy wheels with White diamond finish | £41.67 | £50 | - | - | - | - |
| 16” Steel wheels with White covers | - | - | £41.67 | £50 | - | - |
| 16” Alloy wheels with White diamond finish | - | - | £291.67 | £350 | £41.67 | £50 |
| 16” Alloy wheels with Black diamond finish | - | - | £291.67 | £350 | £41.67 | £50 |
| 16” Alloy wheels with Black diamond finish | £41.67 | £50 | - | - | - | - |
| 17” Alloy wheels with Black diamond finish | £291.67 | £350 | £541.67 | £650 | £291.67 | £350 |
| 17” Alloy wheels with White diamond finish | £291.67 | £350 | £541.67 | £650 | £291.67 | £350 |
| 16” Steel wheels with Black covers | - | - | £41.67 | £50 | - | - |
| Paints |  |  |  |  |  |  |
| Single colour |  |  |  |  |  |  |
| Pastel paint | £0.00 | £0 | £0.00 | £0 | £0.00 | £0 |
| Special Pastel paint | £241.67 | £290 | £241.67 | £290 | £241.67 | £290 |
| Metallic paint | £375.00 | £450 | £375.00 | £450 | £375.00 | £450 |
| Bicolour |  |  |  |  |  |  |
| Special Pastel paint/White roof | £666.67 | £800 | £666.67 | £800 | £666.67 | £800 |
| Metallic paint/White roof | £666.67 | £800 | £666.67 | £800 | £666.67 | £800 |
| Special Pastel paint/Black roof | £666.67 | £800 | £666.67 | £800 | £666.67 | £800 |
| Metallic paint/Black roof | £666.67 | £800 | £666.67 | £800 | £666.67 | £800 |
| Pastel paint/White roof | £666.67 | £800 | £666.67 | £800 | £666.67 | £800 |
| Pastel paint/Black roof | £666.67 | £800 | £666.67 | £800 | £666.67 | £800 |
| Pack |  |  |  |  |  |  |
| Pack Comfort | £166.67 | £200 | £166.67 | £200 | £166.67 | £200 |

Not available –     Standard (